## Slide 1: Automatic Power Factor Correction System Using Arduino
Microcontroller based APFC model.
Improves system power factor.
Uses Arduino, relays, LCD and switching logic.
Simulates industrial APFC behavior.
Displays PF values and capacitor switching stages.

## Slide 2: Introduction
Power factor importance.
Inductive loads cause lagging PF.
Low PF increases losses.
APFC panels correct PF automatically.
Arduino controls capacitor bank switching.

## Slide 3: Objective of the Project
Design Arduino based APFC prototype.
Simulate PF measurement.
Automate relay switching.
Display PF values.
Demonstrate capacitor based correction.

## Slide 4: Block Diagram

## Slide 5: Problem Statement
Industries suffer penalties for low PF.
Manual correction inaccurate.
Reactive power causes inefficiency.
Need automatic microcontroller based correction.

## Slide 6: Components Used Overview
Arduino Uno.
LCD Display.
Relays.
Toggle switch.
Capacitor simulation stages.
LEDs and power supply.

## Slide 7: Arduino Uno Microcontroller
ATmega328P based board.
14 digital I O pins.
6 analog inputs.
Operates at 5V.
Controls relays and LCD.
Central controller of APFC system.

## Slide 8: LCD Module 16x2
Displays PF values.
Shows 'Calculating' messages.
Operates in 4 bit mode.
Used for step by step PF correction display.

## Slide 9: Relay Modules
Used for switching capacitor stages.
Arduino controls relay activation.
One main relay and two correction relays.
Simulates capacitor bank operation.

## Slide 10: Toggle Switch and LED Indicators
Toggle switch selects load type.
Green LED indicates good PF.
Red LED indicates poor PF.
Helps visualize PF correction process.

## Slide 11: Working Principle
Reads switch state.
Generates simulated PF.
Applies capacitor stages.
Displays calculating delay.
Shows corrected PF values.

## Slide 12: Power Factor Simulation Logic
Resistive load PF approx 0.95 0.96.
Inductive load PF between 0.53 0.59.
After each relay activation system waits.
Displays final corrected PF.

## Slide 13: Advantages
Improves understanding of PF.
Simulates industrial APFC.
Low cost educational model.
Easily extendable system.

## Slide 14: Disadvantages
Does not measure real PF.
Only simulation based.
Relays cannot handle high loads.
No CT or PT sensors.

## Slide 15: Applications and Future Scope
Can be used in labs.
Industrial training.
Further development possible.
Add real sensors.
Add IoT monitoring.