## Slide 1: AUTOMATIC THREE PHASE CHANGER USING RELAYS
Automatic Phase Selection and Changeover System
Ensuring uninterrupted power supply
Electrical / Electronics Engineering Project
Circuits Bazaar | Contact: +91-8684-8844-88

## Slide 2: Introduction
Three-phase power systems are widely used in power distribution.
  Most homes and offices use single-phase loads.
  Single-phase failure causes complete power outage.
  Automatic phase changer shifts load to healthy phase.
  Ensures continuity without manual intervention.

## Slide 3: Problem Statement
Frequent phase failures in distribution systems.
  Manual phase shifting is unsafe and unreliable.
  Power remains available in other phases.
  Need for fast and automatic changeover system.
  System must be safe and maintenance friendly.

## Slide 4: Objectives
Provide uninterrupted single-phase power supply.
  Automatically detect phase availability.
  Switch load to next healthy phase.
  Avoid manual switching and human risk.
  Design without microcontroller dependency.

## Slide 5: System Overview
Three input phases continuously monitored.
  Each phase sensed using step-down transformer.
  Relay logic controls phase selection.
  Only one phase connected to load at a time.
  LEDs and buzzer provide status indication.

## Slide 6: Block Diagram
Input: Three Phase AC Supply.
  Step-down transformers for sensing.
  Rectifier and filter circuits.
  Relay driver and relay switching.
  Output: Single-phase load connection.

## Slide 7: Block Diagram

## Slide 8: Circuit Diagram
Complete circuit includes sensing and control.
  Power supply section for control circuit.
  Relay driver using optocoupler and diode.
  Relay contacts handle load switching.
  Diagram space reserved for project circuit.

## Slide 9: Circuit Diagram

## Slide 10: Circuit Diagram

## Slide 11: Circuit Diagram

## Slide 12: Step Down Transformer
Converts 230V AC to low voltage AC.
  Typically steps down to 12V AC.
  Provides electrical isolation.
  Used for phase detection.
  Ensures safety of control circuit.

## Slide 13: Rectifier and Filter Circuit
Diodes convert AC to DC.
  Capacitors smooth the DC output.
  Removes ripple components.
  Provides stable voltage to drivers.
  Essential for reliable operation.

## Slide 14: Voltage Regulator (LM7805)
Provides regulated 5V DC output.
  Protects circuit from voltage variation.
  Used for LEDs and logic components.
  Improves system stability.
  Commonly used linear regulator.

## Slide 15: Relays
Electromagnetic switching devices.
  Allow low voltage control of high power load.
  Ensure electrical isolation.
  Used for automatic phase switching.
  Only one relay active at any time.

## Slide 16: Relay Driver Circuit
Uses transistor BC547.
  Amplifies control signal.
  Flyback diode protects transistor.
  Ensures reliable relay operation.
  Improves switching speed.

## Slide 17: LED Indicators and Buzzer
LEDs indicate phase presence.
  Different colors for each phase.
  Buzzer alerts phase failure.
  Improves safety awareness.
  Provides visual and audio feedback.

## Slide 18: Working Principle
Preferred phase supplies load normally.
  Phase voltage continuously monitored.
  On phase failure relay deactivates.
  Next healthy phase selected automatically.
  Switching occurs within milliseconds.

## Slide 19: Advantages
Uninterrupted power supply.
  Fully automatic operation.
  Simple and reliable design.
  Low maintenance requirement.
  Cost effective solution.

## Slide 20: Applications
Residential buildings.
  Commercial complexes.
  Small and medium industries.
  Hospitals and clinics.
  Rural electrification systems.

## Slide 21: Future Scope
Integration with smart monitoring systems.
  Use of contactors for higher loads.
  Remote monitoring and alerts.
  Solid state switching devices.
  Energy management integration.

## Slide 22: Conclusion
Automatic Three Phase Changer ensures continuity.
  Reduces downtime and human intervention.
  Simple relay-based implementation.
  Highly useful for real-world systems.
  Strong educational and practical value.
Circuits Bazaar | Contact: +91-8684-8844-88