## Slide 1: Underground Cable Fault Locator Using Arduino
Project
@ circuits bazaar, +91-8684884488

## Slide 2
Objective
The objective of this project is to determine the distance of underground cable fault from base station in kilometers. The underground cable system is a common practice followed in many urban areas.
While a fault occurs for some reason, at that time the repairing process related to that particular cable is difficult due to not knowing the exact location of the cable fault. The proposed system is to find the exact location of the fault.
The project uses the standard concept of Ohms law i.e., when a low DC voltage is applied at the feeder end through a series resistor (Cable lines), then current would vary depending upon the location of fault in the cable.

## Slide 3
Introduction
Generally we used to overhead lines. We can easily identify the faults but in rushed places or familiar cities we couldn’t use overhead lines. So, we are moving to underground cables. Underground cables used largely in urban area instead of overhead lines. We can’t easily identify the faults in the underground cables .This project deals with microcontroller, buzzer and LCD.
This proposes greatly reduces the time and operates effectively.

## Slide 4
BLOCK DIAGRAM

## Slide 5
BLOCK DIAGRAM

## Slide 6
CIRCUIT DIAGRAM

## Slide 7
Application
Underground cable fault locator using Arduino is a project that uses the Arduino platform to detect and locate faults in underground power cable networks. This project is designed to detect any faults, such as shorts or breaks in the electrical supply, that may occur in underground power cables. The Arduino board is used to detect the presence of an electrical current in the cable and then determine the location of the fault. The Arduino board is also used to control the operation of the locator so that it can be used to accurately pinpoint the exact fault location. This project can also be used to monitor the status of the power supply and alert the user when any changes occur.

## Slide 8
Future Scope
In the future, this project can be further enhanced to include advanced features such as the ability to detect and report faults in multiple underground cables, the ability to detect and report any changes in the cable power supply, and the ability to detect and report any changes in the environment of the cable network. Additionally, the project can be used to detect and report any changes in the current and voltage of the cable. Finally, the project can be used to detect and report any changes in the temperature of the cable. All these features can be used to make the underground cable fault locator even more powerful and efficient.

## Slide 9
WORKING:-

## Slide 10
Circuit Diagram

## Slide 11
Normally people have been using commercial voltage (230V).This voltage is step-down through step down transformer. Transformer is an electrical device that transfers electrical energy between two or more circuits through electromagnetic induction.. Generally, transformers are used to increase or decrease the voltages of alternating current in electric power applications.These step-down voltage goes to rectifier unit.
Rectifier is nothing but an electronic device which used to convert an AC supply into DC supply. This project we were using bridge rectifier.12V AC supply is converts into 12V DC supply. These voltage moves to the regulator unit. Regulator is an electrical device which is used to maintain a constant voltage. Here we were using two voltage regulator. Namely voltage regulator 7812 and voltage regulator 7805.7812 voltage regulator maintains the 12V DC supply. These voltage is enough to operate relay unit and 7805 voltage regulator maintains the 5V DC supply. These voltage is used to handle the Arduino kit.
WORKING:-

## Slide 12
We uploaded the program in the kit. Program was written if any fault occur in the cable, immediately will open the relay terminal and disconnect that faulty line only. Rest of the other lines operates normally. Now a days embedded system changed metorically.Arduino is the advanced version of embedded system. These Arduino has ample types but we selected Arduino UNO. These Arduino UNO helps to develope many advanced version of ArduinoUNO creates user friendly environment.it easily to adopt other devices using serial port. Next we move the relay.
Relay is nothing but an electrical device here which acted as a switchif any fault occur in the line, will disconnect the line using relay. The connector of the relay moves from normally close conduct to the normally open conducet.we easily find the fault and to disconnect the fault line. Display unit is connect the Arduino kit which is used to where the fault occurs and to display itself
WORKING:-

## Slide 13
HARDWARE COMPONENTS
1.TRANSFORMER (220-12V AC
2.VOLTAGE REGULATOR
3.RECTIFIER
4.FILTER
5.ARDUINO
6.LIQUID CRYSTAL DISPLAY
7.POPO BUTTONS
8.BUZZER
9.POTENTIOMETER
10.RESISTOR
11.DIODE
12.CAPACITOR

## Slide 14
POWER SUPPLY

## Slide 15
POWER SUPPLY
The power supply circuit consists of step down transformer which is 230v step down to 12v.In this circuit 4 diodes are used to form bridge rectifier which delivers pulsating dc voltage & then fed to capacitor filter the output voltage from rectifier is fed to filter to eliminate any a.c. components present even after rectification. The filtered DC voltage is given to regulator to produce 12v constant DC voltage.

## Slide 16
Resistor And Switch Part

## Slide 17
3 Relay Circuit Diagram

## Slide 18
Code of the Project
/* Code copyright to “Circuits Bazaar” for Educational purposes . you can’t use it for commercial purpose */
/*LCD RS pin to digital pin 12
* LCD Enable pin to digital pin 11
* LCD D4 pin to digital pin 7
* LCD D5 pin to digital pin 6
* LCD D6 pin to digital pin 5
* LCD D7 pin to digital pin 4
*/
#include <LiquidCrystal.h>
// initialize the library with the numbers of the interface pins
LiquidCrystal lcd(12, 11, 5, 4, 3, 2)
int sensorPin = A0; // select the input pin for ldr
int sensorValue = 0; // variable to store the value coming

## Slide 19
Code of the Project
void setup() {
pinMode(8, OUTPUT);
pinMode(9, OUTPUT);
pinMode(10, OUTPUT);
digitalWrite(8, LOW);
digitalWrite(9, HIGH);
digitalWrite(10, HIGH);
Serial.begin(9600); //sets serial port for communication
lcd.begin(16, 2);
lcd.print("UNDERGROUND CABLE");
lcd.setCursor(0, 1);
lcd.print("FAULT LOCATOR");
delay(1000);
delay(1000);
}

## Slide 20
Code of the Project
void loop()
{
lcd.clear();
digitalWrite(8, LOW);
digitalWrite(9, HIGH);
digitalWrite(10, HIGH);
delay(350);
sensorValue = analogRead(sensorPin); // read the value from the sensor
Serial.println(sensorValue); //prints the values coming from the sensor on the screen
if( (sensorValue >= 1000) )
{
lcd.setCursor(0, 0);
lcd.print("R - NF,") ;
Serial.print("R - NF,") ;
}

## Slide 21
Code of the Project
else if( (sensorValue >= 890) && (sensorValue <= 920) )
{ Serial.print("R - 2KM,") ;
lcd.setCursor(0, 0);
lcd.print("R - 2KM,") ;
}
else if( (sensorValue >= 870) && (sensorValue <= 880) )
{
Serial.print("R - 4KM,") ;
lcd.setCursor(0, 0);
lcd.print("R - 4KM,") ;
}
else if( (sensorValue >= 800) && (sensorValue <= 825) )
{ Serial.print("R - 6KM,") ;
lcd.setCursor(0, 0);
lcd.print("R - 6KM,") ;
}
else if( (sensorValue >= 670) && (sensorValue <= 688) )
{
Serial.print("R - 8KM,") ;
lcd.setCursor(0, 0);
lcd.print("R - 8KM,") ;
}

## Slide 22
Code of the Project
delay(1500);
digitalWrite(8, HIGH);
digitalWrite(9, LOW);
digitalWrite(10, HIGH);
delay(350);
sensorValue = analogRead(sensorPin); // read the value from the sensor
Serial.println(sensorValue); //prints the values coming from the sensor on the screen

## Slide 23
Code of the Project
if( (sensorValue >= 1000) )
{
Serial.print("Y - NF") ;
lcd.setCursor(8, 0);
lcd.print(" Y - NF,") ;
}
else if( (sensorValue >= 890) && (sensorValue <= 920) )
{ lcd.setCursor(8, 0);
Serial.print("Y - 2KM,") ;
lcd.print(" Y - 2KM,") ;
}

## Slide 24
Code of the Project
else if( (sensorValue >= 870) && (sensorValue <= 880) )
{
Serial.print("Y - 4KM,") ;
lcd.setCursor(8, 0);
lcd.print(" Y - 4KM,") ;
}
else if( (sensorValue >= 800) && (sensorValue <= 825) )
{ Serial.print("Y - 6KM,") ;
lcd.setCursor(8, 0);
lcd.print(" Y - 6KM,") ;
}

## Slide 25
Code of the Project
else if( (sensorValue >= 670) && (sensorValue <= 688) )
{
Serial.print("Y - 8KM,") ;
lcd.setCursor(8, 0);
lcd.print(" Y - 8KM,") ;
}
delay(1500);
digitalWrite(8, HIGH);
digitalWrite(9, HIGH);
digitalWrite(10, LOW);
delay(350);

## Slide 26
Code of the Project
sensorValue = analogRead(sensorPin); // read the value from the sensor
Serial.println(sensorValue); //prints the values coming from the sensor on the screen
if( (sensorValue >= 1000) )
{
lcd.setCursor(5, 1);
Serial.println("B - NF") ;
lcd.print("B - NF") ;
}
else if( (sensorValue >= 890) && (sensorValue <= 920) )
{
Serial.println("B - 2KM") ;
lcd.setCursor(5, 1);
lcd.print("B - 2KM") ;
}

## Slide 27
Code of the Project
else if( (sensorValue >= 870) && (sensorValue <= 880) )
{
Serial.println("B - 4KM") ;
lcd.setCursor(5, 1);
lcd.print("B - 4KM") ;
}
else if( (sensorValue >= 800) && (sensorValue <= 825) )
{ Serial.println("B - 6KM") ;
lcd.setCursor(5, 1);
lcd.print("B - 6KM") ;
}

## Slide 28
Code of the Project
else if( (sensorValue >= 670) && (sensorValue <= 688) )
{
Serial.println("B - 8KM") ;
lcd.setCursor(5, 1);
lcd.print("B - 8KM") ;
}
delay(1500);
}

## Slide 29
CONCLUSION
This paper proposes a technique for locating the distance of fault occurring in underground cable using combination of discrete wavelet transform and traveling wave. Positive sequence current signals are used in fault detection algorithm. It is found that this algorithm can detect fault with the accuracy of 100% using scale 1 only. Using High Resolution Analog to Digital converter the project quality further can be enhanced.