## Slide 1: Advanced Smart Vehicle Safety System
Automatic Headlight Control
Rain Sensing Wiper System
Accident Alert System
Solar Charging System
Arduino Based Vehicle Automation
Developed by: JS Rana
Organization: Circuits Bazaar
Contact: +91-8684-8844-88

## Slide 2: Project Introduction
Modern vehicles require intelligent automation for safety.
Night driving accidents occur due to high beam glare.
Rain reduces visibility and requires quick response.
Accident detection systems are expensive.
This project integrates multiple safety systems into one Arduino platform.
Focus on low cost embedded safety solution.
Educational and industrial relevance.

## Slide 3: Project Objectives
Develop automatic headlight dimmer
Develop rain sensing wiper
Detect accidents using sensors
Provide buzzer alert system
Implement solar charging
Demonstrate embedded automation
Reduce driver workload
Improve safety reliability
Develop scalable vehicle safety platform.

## Slide 4: System Components Overview
Arduino Uno
LDR Sensor
Rain Sensor Module
Reed Switch Accident Sensor
Relay Module
Servo Motor
16x2 LCD Display
Buzzer
Solar Panel
LM317 Charger
Lithium Battery Pack
7805 Voltage Regulator

## Slide 5: Arduino Uno Description
ATmega328P Microcontroller
16 MHz Clock
14 Digital Pins
6 Analog Inputs
5V Operating Voltage
Functions:
Sensor Processing
Decision Making
Motor Control
Relay Switching
Display Communication

## Slide 6: LDR Sensor Working
Light dependent resistor changes resistance with light.
High light intensity reduces resistance.
Arduino reads voltage divider output.
Detects opposite vehicle headlights.
Automatically switches beam.
Prevents glare accidents.
Low cost sensing solution.

## Slide 7: Rain Sensor Module
Detects water droplets.
Conductive plate detects rain.
Comparator converts signal.
Arduino reads analog value.
Activates servo motor.
Demonstrates automatic wiper concept.
Improves visibility safety.

## Slide 8: Servo Motor
PWM controlled motor.
0–180 degree motion.
Simulates windshield wiper.
Low power operation.
Precise angular movement.
Easy Arduino interface.

## Slide 9: Accident Detection System
Magnetic reed switch sensor.
Magnet displacement triggers alert.
Arduino detects signal change.
Buzzer activates.
LCD displays alert.
Basic impact detection model.
Can be expanded with accelerometer.

## Slide 10: Relay Module
Electromechanical switching device.
Allows Arduino to control high power headlights.
High beam and low beam switching.
5V control signal.
Electrical isolation provided.
Safe load switching.

## Slide 11: LCD Display
16x2 alphanumeric display.
Displays system status.
Rain detection message.
Accident alert message.
System ready message.
User feedback interface.

## Slide 12: Solar Charging System
Solar panel converts sunlight to electricity.
LM317 regulates charging voltage.
Charges lithium batteries.
Renewable energy integration.
Improves system sustainability.
Reduces external charging.

## Slide 13: Battery and Power System
18 Lithium ion cells.
Series parallel configuration.
12V output generation.
7805 regulator provides 5V.
Stable microcontroller supply.
Energy storage system.

## Slide 14: Software Used
Arduino IDE
Embedded C Programming
Servo Library
LiquidCrystal Library
Functions:
Sensor reading
Decision logic
Motor control
Display handling
Alert triggering.

## Slide 15: Working Principle
Sensors continuously monitored.
Rain triggers servo wiper.
Accident triggers buzzer.
Light triggers headlight dimming.
LCD shows system state.
Solar charges battery.
Integrated automation workflow.

## Slide 16: Advantages
Improves vehicle safety.
Reduces manual effort.
Automatic operation.
Renewable charging.
Low cost prototype.
Educational value.
Expandable design.
Real time alerts.

## Slide 17: Future Scope
GSM accident messaging.
GPS tracking.
IoT monitoring.
Camera based detection.
AI headlight detection.
Speed monitoring.
Automatic braking.
Mobile application integration.
Raspberry Pi AI upgrade possibility.

## Slide 18: Conclusion
Demonstrates smart vehicle automation.
Combines multiple safety systems.
Low cost implementation.
Scalable architecture.
Educational and research relevance.
Foundation for intelligent vehicle safety systems.
Circuits Bazaar | Contact: +91-8684-8844-88